## Slide 1: Mechanisms Simple Machines
Lever, Wheel and Axle, & Pulley

## Slide 2: Simple Machines
The Six Simple Machines
Mechanisms that manipulate magnitude of force and distance.
Lever
Wheel and Axle
Pulley

## Slide 3: The Six Simple Machines
Inclined Plane
Screw
Wedge

## Slide 4: Mechanical Advantage
Ratio of the magnitude of the resistance and effort forces
Ratio of distance traveled by the effort and the resistance force
Calculated ratios allow designers to manipulate speed, distance, force, and function

## Slide 5: Mechanical Advantage Example
Effort force travels 4 times greater distance than the resistance force.
Magnitude of Force:
Distance Traveled by Forces:
A mechanical advantage of 4:1 tells us
what about a mechanism?
Effort force magnitude is 4 times less than the magnitude of the resistance force.

## Slide 6: Work
The force applied on an object times the distance traveled by the object parallel to the force
Initial position
Final position
Parallel Distance (d║)
Force (F)
Work = Force · Distance = F · d║

## Slide 7: Work
The product of the effort times the distance traveled will be the same regardless of the system mechanical advantage

## Slide 8: Mechanical Advantage Ratios
One is the magic number
If MA is greater than 1:
Proportionally less effort force is required to overcome the resistance force
Proportionally greater effort distance is required to overcome the resistance force
If MA is less than 1:
Proportionally greater effort force is required to overcome the resistance force
Proportionally less effort distance is required to overcome the resistance force
MA can never be less than or equal to zero.

## Slide 9: Ideal Mechanical Advantage (IMA)
Theory-based calculation
Friction loss is not taken into consideration
Ratio of distance traveled by effort and resistance force
Used in efficiency and safety factor design calculations
DR = Distance traveled by resistance force
DE = Distance traveled by effort force

## Slide 10: Actual Mechanical Advantage (AMA)
Inquiry-based calculation
Frictional losses are taken into consideration
Used in efficiency calculations
Ratio of force magnitudes
FE = Magnitude of effort force
FR = Magnitude of resistance force

## Slide 11
Can you think of a machine that has a mechanical advantage greater than 1?
Real World Mechanical Advantage

## Slide 12
Can you think of a machine that has a mechanical advantage less than 1?
Real World Mechanical Advantage

## Slide 13: Lever
A rigid bar used to exert a pressure or sustain a weight at one point of its length by the application of a force at a second and turning at a third on a fulcrum.

## Slide 14: 1st Class Lever
Fulcrum is located between the effort and the resistance force
Effort and resistance forces are applied to the lever arm in the same direction
Only class of lever that can have a MA greater than or less than 1
MA =1
Effort
Resistance
Resistance
Effort
MA <1
Effort
Resistance
MA >1

## Slide 15: 2nd Class Lever
Fulcrum is located at one end of the lever
Resistance force is located between the fulcrum and the effort force
Resistance force and effort force are in opposing directions
Always has a mechanical advantage >1
Resistance
Effort

## Slide 16: 3rd Class Lever
Fulcrum is located at one end of the lever
Effort force is located between the fulcrum and the resistance
Resistance force and effort force are in opposing directions
Always has a mechanical advantage < 1
Resistance
Effort

## Slide 17: Moment
The turning effect of a force about a point equal to the magnitude of the force times the perpendicular distance from the point to the line of action from the force.
M = d x F
Torque: A force that produces or tends to produce rotation or torsion.
Notes: The terms moment and torque are synonymous.

## Slide 18: Lever Moment Calculation
15 lbs
M =
d x F
5.5 in.
Resistance
Effort
Calculate the effort moment acting on the lever above.
Effort Moment =
Effort Moment =
5.5 in. x 15 lb
82.5 in. lb
15 lb

## Slide 19: Lever Moment Calculation
When the effort and resistance moments are equal, the lever is in static equilibrium.
Static equilibrium:
A condition where there are no net external forces acting upon a particle or rigid body and the body remains at rest or continues at a constant velocity.

## Slide 20: Lever Moment Calculation
Resistance
15 lbs
82.5 in.-lb = 36 2/3 lb x DR
Using what you know regarding static equilibrium, calculate the unknown distance from the fulcrum to the resistance force.
Static equilibrium:
Effort Moment = Resistance Moment
5.5 in.
?
15 lb
36 2/3 lb
Effort
82.5 in.-lb /36.66 lb = DR
DR = 2.25 in.

## Slide 21: Lever IMA
Effort
Resistance
DE = 2 π (effort arm length)
Both effort and resistance forces will travel in a circle if unopposed.
Circumference is the distance around the perimeter of a circle.
Circumference = 2 p r
DR = 2 π (resistance arm length)
______________________
IMA =
2 π (effort arm length)
2 π (resistance arm length)

## Slide 22: Lever AMA
The ratio of applied resistance force to applied effort force
5.5 in.
2.25 in.
16 lb
32 lb
Effort
Resistance
What is the AMA of the lever above?
AMA = 2:1
What is the IMA of the lever above?
IMA = 2.44:1
Why is the IMA larger than the AMA?

## Slide 23: Efficiency
In a machine, the ratio of useful energy output to the total energy input, or the percentage of the work input that is converted to work output
The ratio of AMA to IMA
What is the efficiency of the lever on the previous slide? Click to return to previous slide
No machine is 100% efficient.
AMA = 2:1
IMA = 2.44:1

## Slide 24: Wheel & Axle
A wheel is a lever arm that is fixed to a shaft, which is called an axle.
The wheel and axle move together as a simple lever to lift or to move an item by rolling.
It is important to know within the wheel and axle system which is applying the effort and resistance force – the wheel or the axle.
Can you think of an example of a wheel driving an axle?

## Slide 25: Wheel & Axle IMA
DE = π [Diameter of effort (wheel or axle)]
Both effort and resistance forces will travel in a circle if unopposed.
Circumference = 2pr or πd
DR = π [Diameter resistance (wheel or axle)]
______________________
IMA =
π (effort diameter)
π (resistance diameter)
What is the IMA of the wheel above if the axle is driving the wheel?
What is the IMA of the wheel above if the wheel is driving the axle?
6 in. / 20 in. = .3 = .3:1 = 3:10
20 in. / 6 in. = 3.33 = 3.33:1
Ǿ6 in.
Ǿ20 in.

## Slide 26: Wheel & Axle AMA
Ǿ6 in.
Ǿ20 in.
200lb
70lb
What is the AMA if the wheel is driving the axle?
Use the wheel and axle assembly illustration to the right to solve the following.
200lb/70lb = 2.86 = 2.86:1
What is the efficiency of the wheel and axle assembly?
= 85.9%

## Slide 27: Pulley
A pulley is a lever consisting of a wheel with a groove in its rim which is used to change the direction and magnitude of a force exerted by a rope or cable.

## Slide 28: Pulley IMA
Fixed Pulley
- 1st class lever with an IMA of 1
- Changes the direction of force
10 lb
5 lb
5 lb
Movable Pulley
- 2nd class lever with an IMA of 2
- Force directions stay constant
10 lb
10 lb

## Slide 29: Pulleys In Combination
Fixed and movable pulleys in combination (called a block and tackle) provide mechanical advantage and a change of direction for effort force.
If a single rope or cable is threaded multiple times through a system of pulleys,
What is the IMA of the pulley system on the right?
4
Pulley IMA = # strands opposing the
force of the load and
movable pulleys
Notes: Note: The IMA of this system is only about 3.9 because the shortest segment of the rope, tied to the fixed pulley, is not vertical. Since the load is downward, only the upward component of that strand’s force will count, and at the angle shown, the vertical component is about 0.9 times the angled force in that strand. Because resolving a vector into components is not covered until unit 2, this fine point is glossed over at this time.
Could you lift this motorcycle? Ideally, it will take 150 lb of force. A student weighing less than 150 lb could hang on the rope without lifting the motorcycle. This demonstrates an advantage of having the free end pointing upward; then a person can pull with a force greater than their own weight.

## Slide 30: Compound Machines
If one simple machine is used after another, the mechanical advantages multiply.

## Slide 31: Pulleys In Combination
With separate ropes or cables, the output of one pulley system can become the input of another pulley system. This is a compound machine.
40 lbf
40 lbf
20 lbf
20 lbf
10 lbf
10 lbf
What is the IMA of the pulley system on the left?
80 lbf

## Slide 32: Pulley AMA
What is the AMA of the pulley system on the right?
800 lb
230 lb
AMA = 3.48 = 3.48:1
What is the efficiency of the pulley system on the right?
% Efficiency =
= 87%

## Slide 33: Pulley IMA = # strands opposing load only if strands are opposite/parallel to the resistance force.
IMA=2
Calculating IMA
requires trigonometry
Common misconception: Angles don’t matter
Notes: In the pulley on the right, the IMA is not 2. Although the vertical forces from the two strands still are each half the resistance force, the tension in the string depends on the angle. We will not be addressing these types of problems, though you will learn how to do so in unit 2 when you deal with trusses.
In your measurements, keep the strands in the opposite direction from the resistance force to avoid this complication.

## Slide 34: Pulley IMA = # strands opposing the load.
IMA=2
Common misconception:
“Count the effort strand if it pulls up”
sometimes
Count a strand if it opposes the load or the load’s movable pulley. It might pull up or down.
80 lbf
40 lbf
40 lbf
Notes: In the movable pulley here, the effort force is used to pull the movable pulley down along with the load. This is used, for example, in pulling the foot of a sail downward after it has been hoisted. The resistance will only be forced downward 1 ft for every 2 ft of rope pulled out of the system.

## Slide 35: Image Resources
Microsoft, Inc. (2008). Clip art. Retrieved January 10, 2008, from http://office.microsoft.com/en-us/clipart/default.aspx